Danale  Mobile Phone Client Manual

- Download APP

- Software store or apple store search danale

- Scan QR code download

2. Ensure that the camera has been connected to the network, enter the corresponding IP address (the default IP address is 192.168.0.123), and the following interface will pop up. Enter the user name and password (the default user name and password are admin and 123456) and click login to enter the preview interface

Click Configure > Network > P2P, check enable cloud, click save, power off and restart the device. You can see the following screen in the interface. Interface

- Open danale client, click create new account, enter account password and click login after creating successfully;

- After successful login, enter the main interface and click "+" to add the device

5. Add device

- Enter the corresponding WiFi password and click next to search for devices in the LAN. Click "add" to add devices. Then enter the device naming interface, enter the device name, and click "OK". (black solid line added for LAN)

- Click "add QR code", scan the QR code or input the ID of the device to add the device.

Then enter the device naming interface, enter the device name, and click "OK". (the red solid line is added by QR code, and the red dotted line is added by ID)